## Slide 2: Memory Segmentation

## Slide 3
2 Logical Addresses for each Segment
Logical Address – 16 bits
  Base Address (16 bits)
  Offset Address (16 bits)

## Slide 4: Physical Address Calculation

## Slide 5: Memory Address Generation
The BIU has a dedicated adder for determining physical memory addresses.
Physical Address (20 Bits)
Adder
Segment Register (16 bits)
0 0 0 0
Offset Value (16 bits)

## Slide 6: Memory Address Generation
Logical Address is specified as Segment Address : offset Address
Physical address is obtained by shifting the segment address 4 bits to the left and adding the offset address.
Thus the physical address of the logical address A4FB:4872 is:
A4FB0
+ 4872
A9822

## Slide 7: Advantages:
It allows the programmer to access 1MB memory using only 16-bit address.
It allows placing of code, data and stack portions of the same program in different segments, for data and code protection.
It is possible to enhance the memory size of code, data or stack segments beyond 64KB by allotting more than one segment for each area.
It allows to share the data easily.
Disadvantages:
Although the total memory is 16*64KB, at a time only 4*64KB memory can be accessed.

## Slide 8: Architecture of 8086

## Slide 12: Pipelining

## Slide 14: Register Organization

## Slide 19
IP  Offset within the Code segment.
BP  Offset within the Data segment.
SP  Offset within the Stack segment.
SI  Offset within the Data segment.
DI  Offset within the Extra segment.
4.Queue register: Used to store pre-fetched instructions and inputs it to EU.

## Slide 23: Addressing Modes

## Slide 28: Instruction Set